IOC settings :

Motor connections :

Timer settings :

Project manager settings :

Main.c modifications:
* Private includes ----------------------------------------------------------*/
/* USER CODE BEGIN Includes */
#include "stdio.h"
/* USER CODE END Includes */

/* Private typedef -----------------------------------------------------------*/
/* USER CODE BEGIN PTD */

/* USER CODE END PTD */

/* Private define ------------------------------------------------------------*/
/* USER CODE BEGIN PD */
#define TRUE 1
#define FALSE 0
/* USER CODE END PD */

/* Private macro -------------------------------------------------------------*/
/* USER CODE BEGIN PM */

/* USER CODE END PM */

/* Private variables ---------------------------------------------------------*/

/* USER CODE BEGIN PV */
/* control 28BYJ-48 pulse motor with for I/O's for the 4 coils */
/* using a 4 PHASE ULN2003 stepper motor driver PCB */
  enum { A, AB, B, BC, C, CD, D, DA, OFF, NUM_POS } pos;
  uint8_t pinOn[]={ LL_GPIO_PIN_3,
        LL_GPIO_PIN_3 | LL_GPIO_PIN_4,
LL_GPIO_PIN_4,
LL_GPIO_PIN_4 | LL_GPIO_PIN_5,
LL_GPIO_PIN_5,
LL_GPIO_PIN_5 | LL_GPIO_PIN_6,
LL_GPIO_PIN_6,
LL_GPIO_PIN_6 | LL_GPIO_PIN_3};

  uint8_t pinOff[]={ LL_GPIO_PIN_4 | LL_GPIO_PIN_5 | LL_GPIO_PIN_6,
        LL_GPIO_PIN_5 | LL_GPIO_PIN_6,
        LL_GPIO_PIN_3 | LL_GPIO_PIN_5 | LL_GPIO_PIN_6,
        LL_GPIO_PIN_3 | LL_GPIO_PIN_6,
        LL_GPIO_PIN_3 | LL_GPIO_PIN_4 | LL_GPIO_PIN_6,
        LL_GPIO_PIN_3 | LL_GPIO_PIN_4,
 LL_GPIO_PIN_3 | LL_GPIO_PIN_4 | LL_GPIO_PIN_5,
 LL_GPIO_PIN_4 | LL_GPIO_PIN_5,
 LL_GPIO_PIN_3 | LL_GPIO_PIN_4 | LL_GPIO_PIN_5 | LL_GPIO_PIN_6 };
  float time=0.0f;

typedef struct { float sec;
        float frequency;
        } speedPoint;

speedPoint curve[4] = {{0.0f,0.0f},{10.0f,400.0f},{30.0f,400.0f},{40.0f,0.0f}};
uint8_t pulseCounter=0;
volatile uint8_t enabled=FALSE;

/* USER CODE END PV */

/* Private function prototypes -----------------------------------------------*/
void SystemClock_Config(void);
static void MX_GPIO_Init(void);
static void MX_TIM2_Init(void);
/* USER CODE BEGIN PFP */

// helper function to send printf() output to the SWV ITM Data Console
int __io_putchar(int ch)
{
ITM_SendChar(ch);
return ch;
}

// Callback function called when timer TIM2 creates update event
// In essence this means count has reached the auto reload value
// My STM32F407VET6 runs on 16 MHz
// TIM 2 has a prescaler of 16 so its base frequency is 1MHz.
// there for to obtain a frequency of f Hz we need to set ARR to 1000000/f;
void TIM2_Update()
{
  if (enabled==TRUE)
  {
  LL_GPIO_ResetOutputPin(IN1_GPIO_Port,pinOff[pulseCounter]);
  LL_GPIO_SetOutputPin(IN1_GPIO_Port,pinOn[pulseCounter]);
  pulseCounter=(pulseCounter + 1) % (NUM_POS-1);
  }
  else
  {
  LL_GPIO_ResetOutputPin(IN1_GPIO_Port,pinOff[OFF]);
  }
}

// interpolate on the curve to get the required motor speed.
void interpol_speed(float sec, speedPoint curve[], uint32_t curveSize, float *frequency,volatile uint8_t *enabled)
{
*enabled=FALSE;
if (curveSize==0)
{
frequency=0;
return;
}
if (sec<=curve[0].sec)
{
*frequency=curve[0].frequency;
    return;
}

if (curve[curveSize-1].sec<=sec)
{
*frequency=curve[curveSize-1].frequency;
    return;
}
*enabled=TRUE;
for (int i=0;i<curveSize-1;i++)
{
if (curve[i].sec==sec)
{
*frequency=curve[i].frequency;
return;
}
if (curve[i].sec<sec && sec<=curve[i+1].sec)
{
speedPoint *a=&curve[i];
speedPoint *b=&curve[i+1];
*frequency=a->frequency+ (b->frequency-a->frequency)/(b->sec-a->sec)*(sec-a->sec);
return;
}
}
}

/* USER CODE END PFP */

/* Private user code ---------------------------------------------------------*/
/* USER CODE BEGIN 0 */

/* USER CODE END 0 */

/**
  * @brief The application entry point.
  * @retval int
  */
int main(void)
{
  /* USER CODE BEGIN 1 */

  /* USER CODE END 1 */

  /* MCU Configuration--------------------------------------------------------*/

  /* Reset of all peripherals, Initializes the Flash interface and the Systick. */
  LL_APB2_GRP1_EnableClock(LL_APB2_GRP1_PERIPH_SYSCFG);
  LL_APB1_GRP1_EnableClock(LL_APB1_GRP1_PERIPH_PWR);

  /* System interrupt init*/
  NVIC_SetPriorityGrouping(NVIC_PRIORITYGROUP_4);

  /* SysTick_IRQn interrupt configuration */
  NVIC_SetPriority(SysTick_IRQn, NVIC_EncodePriority(NVIC_GetPriorityGrouping(),15, 0));

  /* USER CODE BEGIN Init */

  /* USER CODE END Init */

  /* Configure the system clock */
  SystemClock_Config();

  /* USER CODE BEGIN SysInit */

  /* USER CODE END SysInit */

  /* Initialize all configured peripherals */
  MX_GPIO_Init();
  MX_TIM2_Init();
  /* USER CODE BEGIN 2 */

  LL_TIM_EnableIT_UPDATE(TIM2);
  LL_TIM_EnableCounter(TIM2);

  /* USER CODE END 2 */

  /* Infinite loop */
  /* USER CODE BEGIN WHILE */
  while (1)
  {
    /* USER CODE END WHILE */

    /* USER CODE BEGIN 3 */
float frequency;
    // calculate the new frequency needed at time s:
    interpol_speed(time, curve, sizeof(curve)/sizeof(curve[0]), &frequency,&enabled);
    if (enabled && frequency > 0.01f)
    // reload TIM2 with new value:
    LL_TIM_SetAutoReload(TIM2, 1.0E6f/frequency);
    if ((int) (10*time) % 10==0)
    printf("Time = %f, frequency = %.2f Hz, enabled = %d \n",time, frequency, enabled);
    if (time > curve[3].sec)
    {
    // wait a bit and restart the cycle
    LL_mDelay(5000);
    printf("Restarting the cycle:\n");
    time=0.0f;
    }
    LL_mDelay(100);
    time=time+0.100f;
  }
  /* USER CODE END 3 */
}

Main.h modifications:

/* Exported types ------------------------------------------------------------*/
/* USER CODE BEGIN ET */
void TIM2_Update();
/* USER CODE END ET */

Stm32f4xx_it.c modifications:
/******************************************************************************/
/* STM32F4xx Peripheral Interrupt Handlers */
/* Add here the Interrupt Handlers for the used peripherals. */
/* For the available peripheral interrupt handler names, */
/* please refer to the startup file (startup_stm32f4xx.s). */
/******************************************************************************/

/**
  * @brief This function handles TIM2 global interrupt.
  */
void TIM2_IRQHandler(void)
{
  /* USER CODE BEGIN TIM2_IRQn 0 */
  uint8_t UIF=LL_TIM_IsActiveFlag_UPDATE(TIM2);
  if (UIF)
  {
TIM2_Update();
LL_TIM_ClearFlag_UPDATE(TIM2);
  }
  /* USER CODE END TIM2_IRQn 0 */
  /* USER CODE BEGIN TIM2_IRQn 1 */

  /* USER CODE END TIM2_IRQn 1 */
}

/* USER CODE BEGIN 1 */

/* USER CODE END 1 */

Debug output :